## Slide 1: Seed Sowing Robot GROUP (5)
SEED SOWING ROBOT
NAME | ID
Assem Yasser Mohamed Elsharbeiny | 80681
Khaled Abdelnasser Elshamndy | 80768
Omar Ashraf Abdelmawgoud | 80601
Mohamed Ahmed Mohamed Khater | 79573
Mohamed Kamal Ali Ahmed | 80651
Seed Sowing Robot GROUP (5)
NAME | ID
Assem Yasser Mohamed Elsharbeiny | 80681
Khaled Abdelnasser Elshamndy | 80768
Omar Ashraf Abdelmawgoud | 80601
Mohamed Ahmed Mohamed Khater | 79573
Mohamed Kamal Ali Ahmed | 80651

## Slide 2: AGENDA
The calculations of motor sizing, chassis, load
CALCULATIONS
01
The parts of each component with sizes
MECHANICAL DESIGN
02
The simulation of the robot on RVz
SIMULATION
04
Components of the circuit and the main circuit
ELECTRICAL CIRCUIT
03
05
NAVIGATION
Robot Navigation Process
06
SOFTWARE
Arduino, ESP32 and Raspberry Pi
INTRODUCTION
Introduction of Robot and Objective
07
SEED SOWING ROBOT

## Slide 3: INTRODUCTION
01
SEED SOWING ROBOT

## Slide 4: INTRODUCTION and OBJECTIVE
SEED SOWING ROBOT
The seed sowing robot project revolutionizes the traditional method of manual seed sowing in agriculture by automating the process and reducing human effort. By leveraging cutting-edge technologies like ROS, mapping, localization, and path planning, the robot achieves efficient and accurate seed placement, optimizing crop yields and promoting sustainable farming practices.

## Slide 5: STEPS OF IMPLEMENTAION
SEED SOWING ROBOT

## Slide 6: CALCULATIONS
02
SEED SOWING ROBOT

## Slide 7: Motor sizing
SEED SOWIG ROBOT
mgx = mg * sin (ɵ)
mgy = mg * cos (ɵ)
Torque for each motor
Total power (P) per motor can be calculated using the following relation:
P = T * w = 1 *13.1 = 13.1 W
Maximum current (I) requirements:
I = P/V =1.19 A
The capacity (c) of battery pack required can be estimated using the equation:
𝑐 = 𝐼 ∗ 𝑡 ∗ 𝑁 = 4.86 Ah
Parameters | Values
Total mass | 15 Kg
Pay load | 7 kg
RPM | 125
Num . Of Driver motors | 4
Radius of drive wheel | 0.065 m
Desired Acceleration | 0.2 m/
Angular velocity | 13.1 rad/s
Max . Incline angle | 20ᵒ
Supply voltage | 12v
Desired operating time | 1 hour
Total efficiency | 80%
Parameters | Values
Total mass | 15 Kg
Pay load | 7 kg
RPM | 125
Num . Of Driver motors | 4
Radius of drive wheel | 0.065 m
Desired Acceleration | 
Angular velocity | 13.1 rad/s
Max . Incline angle | 20ᵒ
Supply voltage | 12v
Desired operating time | 1 hour
Total efficiency | 80%

## Slide 8: CALCULATION VALIDATION
SEED SOWIG ROBOT

## Slide 9: DESIGN OF AUGER
The auger has speed range 50-150 rpm
Pitch = 10 mm
d = 10 mm
D = 30 mm
SEED SOWIG ROBOT
=360 – 354 =5.9
Screw discharge (capacity) = 50 𝑘𝑔/ℎ

## Slide 10: Static and fatigue stress analysis for chassis
SEED SOWIG ROBOT
Bending stress that applied on chassis
Length = 0.51 m
The force applied on chassis = 140 N
() = 276 MPa

## Slide 11: MECHANICAL DESIGN
03
SEED SOWING ROBOT

## Slide 12: EXPLODED PARTS OF ROBOT
SEED SOWING ROBOT

## Slide 13: Assembly with table of parts
SEED SOWING ROBOT

## Slide 14: ASSEMBLY’S DIMENSIONS
SEED SOWING ROBOT

## Slide 15: CHASSIS’S DIMENSIONS
SEED SOWING ROBOT

## Slide 16: COVER’S DIMENSIONS
SEED SOWING ROBOT

## Slide 17: DRILL’S DIMENSIONS
SEED SOWING ROBOT

## Slide 18: LEVELER’S DIMENSIONS
SEED SOWING ROBOT

## Slide 19: FUNNEL’S DIMENSIONS
SEED SOWING ROBOT

## Slide 20: DRILL HOLDER’S DIMENSIONS
SEED SOWING ROBOT

## Slide 21: DRILL HOLDER’S DIMENSIONS
SEED SOWING ROBOT

## Slide 22: MOTOR HOLDER’S DIMENSIONS
SEED SOWING ROBOT

## Slide 23: WHEEL MOTOR’S DIMENSIONS
SEED SOWING ROBOT

## Slide 24: DC MOTOR’S DIMENSIONS
SEED SOWING ROBOT

## Slide 25: PLATE’S DIMENSIONS
SEED SOWING ROBOT

## Slide 26: TANK’S DIMENSIONS
SEED SOWING ROBOT

## Slide 27: WHEEL’S DIMENSIONS
SEED SOWING ROBOT

## Slide 28: ELECTRICAL CIRCUIT
04
SEED SOWING ROBOT

## Slide 29
SEED SOWING ROBOT
Component | Quantity
Raspberry Pi 4 Model B | 1
ESP32 microcontroller | 1
Arduino Mega | 1
RPLidar A1M8 LiDAR sensor | 1
DC Motor with Gearbox 12V | 4
Servo motor SG90 | 3
Cytron MDD 10A motor drivers | 2
MPU9250 sensor (accelerometer and gyroscope) | 1
12V lithium-ion DC battery | 1
Emergency button | 1
DC to DC buck converter | 1
TFT LCD display | 1
External Rotary Encoder | 4
4*3 Keypad | 1
Water pump 12V | 1
Moisture Sensor | 1
Level Sensor | 1
relay module | 1
L298N Driver Motor | 1
Wire connectors | -
Current sensor | 1
DC motor With encoder | 2
DC motor with gearbox | 1
ELECTRICAL CIRCUIT

## Slide 30: ELECTRICAL CIRCUIT
SEED SOWIG ROBOT

## Slide 31: NAVIGATION
05
SEED SOWING ROBOT

## Slide 32
What is gmapping:
gmapping ROS package is an implementation of a specific SLAM algorithm called gmappin.
Hardware Requirements configuration:
Provide Good Laser Data
Provide Good Odometry Data

## Slide 33: Gmapping
SEED SOWING ROBOT

## Slide 34: AMCL
SEED SOWING ROBOT
Hardware Requirements:
Provide Good Laser Data
Provide Good Odometry Data
Provide Good Laser-Based Map Data
OUTPUT:
AMCL outputs an estimated pose of the robot. The more the robot moves around the environment, the more data the localization system will get, so the more precise the estimated pose it returns will be

## Slide 35: Navigation stack
SEED SOWING ROBOT

## Slide 36: Sensor fusion
SEED SOWING ROBOT

## Slide 37: SIMULATION
06
SEED SOWING ROBOT

## Slide 38: SIMULATION
SEED SOWING ROBOT
Key Benefits of Robot Simulation:
1-Visualization and debugging:
Running a simulation provides all the information you need about the environment and the robot.
2-Fail fast, learn faster:
Failing on a simulated robot is faster and cheaper.
3-Building a robot is too expensive :
test algorithms on a real robot is too expensive.

## Slide 39
SEED SOWING ROBOT
Steps of simulation
1- Build a Robot:
URDF(XACRO).
Adding gazebo plugins.
2- Connect to ROS:
Gazebo's ROS node.
The gazebo service node
/gazebo/spawn_urdf_model.
3-launch gmapping.launch
4-launch amcl.launch
5-launch navigation.launch

## Slide 40
SEED SOWING ROBOT
URDF

## Slide 41
SEED SOWING ROBOT
TF

## Slide 42
SEED SOWING ROBOT
TF

## Slide 43
SEED SOWING ROBOT
GAZEBO WORLDS

## Slide 44
SEED SOWING ROBOT
MAPS

## Slide 45
SEED SOWING ROBOT
LOCALIZATION

## Slide 46
SEED SOWING ROBOT
NAVIGATION

## Slide 47
SEED SOWING ROBOT
NAVIGATION

## Slide 48: SOFTWARE
07
SEED SOWING ROBOT

## Slide 49
SEED SOWING ROBOT
Communication
Rosserial:
Rosserial bridges the communication gap between ROS and microcontrollers, which are often used in embedded systems to control sensors, actuators, and other hardware components
SSH(Secure Shell Protocol) :
is a remote administration protocol that allows users to access, control, and modify their remote servers over the internet.
EX:
SSH –Y ubuntu@IP

## Slide 50
SEED SOWING ROBOT
System configuration

## Slide 51
SEED SOWING ROBOT
layout

## Slide 52
SEED SOWING ROBOT
layout

## Slide 53
SEED SOWING ROBOT
Rqt Graph

## Slide 54
SEED SOWING ROBOT
THANKS